## Slide 1
How to use the BEM class
root: str
file_airfoil: str,
save_dir: str
BEM()
BEM object
rotor_radius: float,
root_radius: float
n_blades: int,
air_density: float
.set_constants()
wind_speed: float
tip_speed_ratio: float
pitch: float
.solve()
results: dict
Documentation for non-trivial function inputs:
BEM:
  root: string to directory in which the airfoil file and the results directory is
  file_airfoil: filename with filetype as string
  save_dir: directory name of results as string
.set_constants:
  All radii in metre.
  Air density in kg/m3
solve:
  pitch: in degree
  Remaining values that are pre-set are explained later
Dictionary key | Explanation
positions | Radial positions in m
a | Axial induction factor
a_prime | Tangential induction factor
f_n | Normal load in N/m
f_t | Tangential load in N/m
bec | Blade end correction (see next slide)
start

## Slide 2
What solve() does
The numerical approach needed for equating the loads of the blade element and momentum theory is not done explicitly, but implicitly by solving a root finding problem for the difference of thrust coefficient coming from both theories. Here, it is implicit because scipy methods for root finding are used. These functions require, amongst other parameters, the function of which the root is to find as input.
.solve()
Loop radially over blade elements
results: dict
Step | Action | Function name
1 | Get chord | ._get_chord
2 | Get twist | ._get_twist
3 | Get local solidity | ._local_solidity
4 | Define function for root problem | residue (explained next slide)
4 | Get induction factor (solve root problem) | brentq or newton
5 | Translate induction factor to values of interest | ._phi_to_aero_values and local calcuations
6 | Return values of step 5 | ._update_a_prime

## Slide 3
What residue() does
._phi()
The function residue() receives an axial induction factor a as input and returns the difference between the C_T from momentum theory and blade element theory that follows for the current a.
a: float
a_prime: float,
wind_speed: float
rotational_speed: float
radius: float
phi: float
._phi_to_areo_values()
a_prime: float,
twist: float
pitch: float,
radius: float
tip_speed_ratio: float,
blade_end_correction_type: str,
root: bool
tip: bool
._update_a_prime()
c_n: float,
c_t: float,
bec: float
._equate_blade_element_and_momentum()
a: float
glauert_correction: str,
a: float,
blade_end_correction: float,
phi: float,
local_solidity: float,
c_normal: float
Non-trivial inputs:
blade_end_correction_type: string of which university uses which correction
tip, root: Boolean of whether to use correction for tip, root, respectively
glauert_correction: like blade_end_correction_type